Preamble

1.	Register File

The Register File is made up of seven (7) general purpose registers labeled A through G. Each register can hold 8 bits (1 byte). Registers F (lo byte) & G (hi byte) can be accessed together as a 16 bit memory address register labeled as MA.

The Register File has one write port, RW and two read ports, RP1 & RP2. This allows you to choose two registers for operands to the ALU and branching circuits as well as write a result back to a third register.

RW = write result port
RP1 = first operand port
RP2 = second operand port

2.	Control Word

The Control Word is made up of 32 bits (4 bytes) that are aligned on 4 byte boundaries. Each clock cycle increments the Program Counter (PC) by one (1) allowing the next Control Word to issue forth. Two (1) Control Word IS required per instruction making each instruction take ONE (1) clock cycle to complete.

The first two (2) bytes of the Control Word contain the OpCode, the immediate toggle bit as well as the register selection bits. These two bytes are organized as follows:

16 Byte 2	8|7 Byte 1	0

 RW:3, RP1:3, RP2:2 | RP2:1, ImmSel:1, OpCode:6

There are 3 types of Control Words all made up of 32 bits (4 bytes):

Register Type:

00000000|00000000|www11122|2txxxxxx

Immediate Data Type:

00000000|iiiiiiii|www11122|2txxxxxx

Immediate Address Type:

iiiiiiii|iiiiiiii|www11122|2txxxxxx

where:

i = Immediate Value
w = RW Register Code
1 = RP1 Register Code
2 = RP2 Register Code
t = Immediate Toggle (1 = immediate value, 0 = no immediate value)
x = Instruction OpCode
0 = No Value

As each byte is stored in a separate 8 bit FLASH memory, RP2 will need to be split in the compiler so that the first bit goes to the first FLASH chip with the remaining two bits going into the second FLASH chip as described by | character used in the full Control Words shown previously.

3.	Parallel Ports

There are two parallel ports (PP1 & PP2) attached that utilize bus transceivers and a status register (PS) to control communication and access to peripheral devices.

4.	LABEL

A LABEL statement inside the assembly code file is used for jumping and branching. Each LABEL is unique and marks the address in program memory where the following code begins. This allows for program control and provides an easy way to move around code in loops. It also provides a human readable way to think in functions or sub routines. A LABEL statement is typed on its own line and should begin with the : character and contain no spaces, as follows:

:Start
ldr A,5
beq A,5,Start
Instruction Set

1.	LDR – Load Register

1.1	Description

This instruction loads an 8-bit value into a general purpose register from many potential sources. It also can load a 16-bit value in to the memory address register (ma):

ldr RW,Imm

- Loads a register RW with an 8 bit immediate value

Control Word:

00000000|iiiiiiii|www00000|01000001

ldr RW,Adrs

- Loads a register RW with an 8 bit value from RAM addressed by an immediate 16 bit value in HEX

Control Word:

iiiiiiii|iiiiiiii|www00000|00000010

ldr RW,ma

- Loads a register RW with an 8 bit value from RAM addressed by a 16 bit value stored in registers F & G

Control Word:

00000000|00000000|www00000|00000011

ldr RW,PPX

- Loads a register RW with an 8 bit value from a parallel port

Control Word:

00000000|00000000|www00000|00xxxxxx

ldr ma,Adrs(LABEL)

- Loads register ma with a 16 bit immediate value

Control Word:

00000000|00000000|www00000|00000101
2.	STR – Store Register

2.1	Description

This instruction stores a value from a register into RAM as follows:

str RP2,Adrs

- Stores a register RP2 with an 8 bit value to RAM addressed by an immediate 16 bit value in HEX

Control Word:

iiiiiiii|iiiiiiii|00000022|20000110

str RP2,ma

- Stores a register RP2 with an 8 bit value to RAM addressed by a 16 bit value stored in registers F & G

Control Word:

00000000|00000000|00000022|20000111

str RP2,PPX

- Stores a register RP2 with an 8 bit value to a parallel port

Control Word:

00000000|00000000|00000022|20xxxxxx

3.	CPR – Copy Register to Register

3.1	Description

This instruction copies one register to another:

cpr RP2,RW

- copies a register RP2 to another register RW

Control Word:

(1) 00000000|00000000|www00022|20001000

4.	JMP & JCF – Jump to LABEL & Jump if Carry Flag Set

4.1	JMP Description

This instruction jumps in program memory to an address represented by a LABEL statement and calculated in the compiler. See LABEL in the Preamble section above for more info on how this works.

jmp LABEL

- jumps to an address represented by the LABEL statement

Control Word:

iiiiiiii|iiiiiiii|00000022|21xxxxxx

4.2	JCF Description

This instruction jumps if the carry flag is set to an address in program memory that is represented by a LABEL statement and calculated in the compiler. This instruction does not have to immediately follow an add instruction as the carry flag stays set until the next add/sub instruction. See LABEL in the Preamble section above for more info on how the addressing works.

jcf LABEL

- jumps if the carry flag is set to an address represented by the LABEL statement

Control Word:

iiiiiiii|iiiiiiii|00000022|21xxxxxx

5.	BLT – Branch if Less Than

5.1	Description

This instruction branches if less than:

blt RP1,RP2,LABEL

- Branches if RP1 is less than RP2 to an immediate address

Control Word:

iiiiiiii|iiiiiiii|00011122|20001100

blt RP1,Imm,MA

- Branches if RP1 is less than Imm to an address held in MA

Control Word:

00000000|00000000|00000022|21001101

6.	BLE – Branch if Less Than or Equal To

6.1	Description

This instruction branches if less than:

blt RP1,RP2,LABEL

- Branches if RP1 is less than RP2 to an immediate address

Control Word:

iiiiiiii|iiiiiiii|00011122|20xxxxxx

blt RP1,Imm,MA

- Branches if RP1 is less than Imm to an address held in MA

Control Word:

00000000|00000000|00000022|21xxxxxx

7.	BEQ – Branch if Equal To

7.1	Description

This instruction branches if less than:

blt RP1,RP2,LABEL

- Branches if RP1 is less than RP2 to an immediate address

Control Word:

iiiiiiii|iiiiiiii|00011122|20xxxxxx

blt RP1,Imm,MA

- Branches if RP1 is less than Imm to an address held in MA

Control Word:

00000000|00000000|00000022|21xxxxxx

8.	BNE – Branch if Not Equal To

8.1	Description

This instruction branches if less than:

blt RP1,RP2,LABEL

- Branches if RP1 is less than RP2 to an immediate address

Control Word:

iiiiiiii|iiiiiiii|00011122|20xxxxxx

blt RP1,Imm,MA

- Branches if RP1 is less than Imm to an address held in MA

Control Word:

00000000|00000000|00000022|21xxxxxx

9.	BGE – Branch if Greater Than or Equal To

9.1	Description

This instruction branches if less than:

blt RP1,RP2,LABEL

- Branches if RP1 is less than RP2 to an immediate address

Control Word:

iiiiiiii|iiiiiiii|00011122|20xxxxxx

blt RP1,Imm,MA

- Branches if RP1 is less than Imm to an address held in MA

Control Word:

00000000|00000000|00000022|21xxxxxx

10.	BGT – Branch if Greater Than

10.1	Description

This instruction branches if less than:

blt RP1,RP2,LABEL

- Branches if RP1 is less than RP2 to an immediate address

Control Word:

iiiiiiii|iiiiiiii|00011122|20xxxxxx

blt RP1,Imm,MA

- Branches if RP1 is less than Imm to an address held in MA

Control Word:

00000000|00000000|00000022|21xxxxxx

11.	ADD – Addition

11.1	Description

This instruction adds two operands provided as arguments and stores the result in a register identified by a third argument RW. The first operand is RP1 and the second operand can either be sourced from RP2 or an immediate value as described below:

ADD RP1,RP2,RW

- Add RP1 and RP2 and store in RW

Control Word:

00000000|00000000|www11122|20011000

ADD RP1,Imm,RW

- Add RP1 and an immediate values and store in RW

Control Word:

00000000|iiiiiiii|www11100|01011001

12.	SUB – Subtraction

12.1	Description

This instruction subtracts two operands provided as arguments and stores the result in a register identified by a third argument (RW). The first operand is RP1 and the second operand can either be sourced from RP2 or an immediate value as described below:

SUB RP1,RP2,RW

- Subtract RP1 and RP2 and store in RW

Control Word:

00000000|00000000|www11122|20011010

SUB RP1,Imm,RW

- Subtract RP1 and an immediate values and store in RW

Control Word:

00000000|iiiiiiii|www11100|01011011

13.	AND – Logical AND

13.1	Description

This instruction performs a logic AND on two operands provided as arguments and stores the result in a register identified by a third argument (RW). The first operand is RP1 and the second operand can either be sourced from RP2 or an immediate value as described below:

AND RP1,RP2,RW

- Perform a logical AND on RP1 and RP2 and store in RW

Control Word:

00000000|00000000|www11122|20

AND RP1,Imm,RW

- Perform a logical AND on RP1 and an immediate values and store in RW

Control Word:

00000000|iiiiiiii|www11100|01